Bench Seating Brackets.

# Cantilever Frame

This frame is used where a bench seat is required on a wall. It is bolted into the wall using two special anchor bolts (supplied in the pack). The frame will accomodate 13mm thick compact laminate seat material or alternatively wooden seats such as mahogany or ash.

The design is such that every surface is subject to a four stage coating process to ensure maximum resistance to corrosion, even in wet areas such as swimming pools.

The frames should be mounted no more than one metre apart to ensure the seat material does not break under extreme loading.

The frame is fitted with a seperate top mounting plate. This plate has three pairs of mounting holes for the seat material.

All fixings are included in the pack and full installation instructions are available. If you wish to mount the frame on a cubicle, or back to back through a panel, we have the correct fixings available.  Please call for details.

We use the highest quality material in the construction of their bench seating, a combination of 1.6mm thick ERW tube and CR4 steel plate is used to ensure maximum corrosion resistance. Once fabricated, all parts are processed through a four stage phosphating and paint plant guaranteeing maximum corrosion resistance and

longevity of service.The frames are available from stock in a textured powder coat finish.

# Wall Mount Frame

This frame is used when it is not possible to use a cantilever frame, for example there may be services running around the walls, such as pipes. It can also be used when the wall is not sufficiently strong enough to hold the cantilever frame. It is bolted into the wall using two special anchor bolts and fixed to the floor using an adjustable foot and holding down bracket (supplied in the pack).

The frame will accomodate 13mm thick compact laminate seat material or alternatively wooden seats such as mahogany or ash.

The design is such that every surface is subject to a four stage coating process to ensure maximum resistance to corrosion, even in wet areas such as swimming pools.

The frames should be mounted no more than one metre apart to ensure the seat material does not break under extreme loading.

The frame is fitted with a seperate top mounting plate. This plate has three pairs of mounting holes for the seat material.

# Double Island Frame

Click thumbnail to enlarge

Similair to a single island frame, the double island frame incorporates an additional upright section to mount a back rest and hat and coat hook rail. This frame is normally placed freestanding on the floor, or extending from a wall. The back to back seating arrangement makes optimal use of floor space. Usually combined with the single island and cantilever or wall mount frames to complete the room.

The frame is assembled to the next frame using a special tie bar. Long lengths can be built by adding additional frames and tie bars. Where specific room sizes need to be accomodated, it is necessary for the tie bars to be manufactured to order. Our technical team are able to calculate the exact sizes for you.

The frame is supplied with adjustable feet and fixing down brackets as well as special floor anchors which are used to secure the seat once it is in position.

The frame will accomodate 13mm thick compact laminate seat material or alternatively wooden seats such as mahogany or ash.

The design is such that every surface is subject to a four stage coating process to ensure maximum resistance to corrosion, even in wet areas such as swimming pools.

The frames should be mounted no more than one metre apart to ensure the seat material does not break under extreme loading.

The frame is fitted with a seperate top mounting plate. This plate has three pairs of mounting holes for the seat material.

Slats Options:

a). Compact grade laminate plank 300/400mm wide through fixed with stainless hex screws.

b) Compact grade slats 75mm wide bull nosed fixed with hex screws.

c) Solid wood slats 50x25mm fixed with stainless steel wood screws.

Most standard laminate colours available ( compact laminate always has black edge ).

Solid wood slats avaible in oak, ash, walnut and other on request.