K32 PANEL CUBICLES

To be read with preliminaries and general conditions

Manufacturer:Toilet Cubicles Ireland, Unit 15 Donore Business Pk, Donore rd, Drogheda Co Louth ph/fax 041-9818148

Email: info@toiletcubiclesireland.ie Web: www.toiletcubiclesireland.ie

Product reference: form toilet cubicles

Doors: 18mm/25mm chipboard faced both sides with high pressure laminate (HPL)

Core material: High density chipboard

Finish: Subject to HPL manufacturer selected

Colour: Toilet cubicles Ireland HPL selection or specified colours subject to size

Edge treatment: Square lipped to match or contrast face surface in 1mm PVC or HPL

Panels: 25mm chipboard faced both sides with high pressure laminate (HPL)

Core material: High density chipboard

Finish: Subject to HPL manufacturer selected

Colour: Toilet Cubicles Ireland HPL selection or specified colours subject to size

Edge treatment: Leading edge of the extended partition bull-nosed to 180 degree profile, all other edges are lipped square match or contrast face surface in 1mm PVC or HPL

Pilasters: Two formed stainless steel angle profiles fixed to either side of the partition and set back from leading edge. Vertical edges full radius for safety

Head Rail: 25mm diameter stainless steel tube fixed between partitions

Finish: Satin polished

Legs: Slim-line, adjustable cylindrical design, with concealed fixings positioned in line with the pilaster angles fixed directly into the partition core.

Ironmongery & Accessories: Adjustable pivot hinges/Buffered coat hook/DDA compliant lever operated indicator bolt with circular face plate and emergency release facility/Concealed continuous ‘T’ section partition fixings.

Finish/ Colour: Stainless steel or stainless steel effect

Dimensions: Unless stipulated here dimensions are as the technical data provided for form

Other requirements: Complete with outward opening doors to ambulant and enlarged cubicles as requested. Cubicles with inward opening doors can be set out to maintain 450mm diameter manoeuvring space within the cubicle, this may require an extended pilaster detail. Optional door material veneer or glass at surcharge