K32 PANEL CUBICLES

To be read with preliminaries and general conditions

Manufacturer: Toilet Cubicles Ireland, Unit 15, Donore Business pk, Donore Rd, Drogheda, Co LouthPh/fax 041-9818148

Email: info@toiletcubiclesireland.ie Web: www.toiletcubiclesireland.ie

Product reference: form+ toilet cubicles

Pilasters: Two formed stainless steel angle profiles fixed to either side of the partition and set back from leading edge. Vertical edges full radius for safety.

Head Rail: 25mm diameter stainless steel tube fixed between partitions

Finish: Satin polished

Doors: 12/13mm solid grade laminate (SGL) same colour both sides

Core material: Not required self supported board black core (SGL)

Finish: Subject to SGL manufacturer selected

Colour:Toilet Cubicles Ireland SGL selection or specified colours subject to size

Edge treatment: Machined smooth profile or square (Black core always visible)

Panels: 12/13mm solid grade laminate (SGL) same colour both sides

Core material: Not required self supported board black core (SGL)

Finish: Subject to SGL manufacturer selected

Colour: Toilet Cubicles Ireland SGL selection or specified colours subject to size

Edge treatment: Machined smooth profile or square (Black core always visible)

Legs: Slim-line, adjustable cylindrical design, with concealed fixings positioned in line with the pilaster angles fixed directly into the partition core.

Ironmongery & Accessories: Adjustable pivot hinges/Buffered coat hook/DDA compliant lever operated indicator bolt with circular face plate and emergency release facility, bracket fixings to wall and pilaster

Finish/ Colour: Stainless steel or stainless steel effect.

Dimensions: Unless stipulated here dimensions are as the technical data provided for form+

Other requirements: Complete with outward opening doors to ambulant and enlarged cubicles as requested. Cubicles with inward opening doors can be set out to maintain 450mm diameter manoeuvring space within the cubicle, this may require an extended pilaster detai