K32 PANEL CUBICLES

To be read with preliminaries and general conditions

Manufacturer: Toilet Cubicles Ireland, Unit 15, Donore Business pk, donore rd, Drogheda, Co Louth Ph/ fax:041-9818148.

Email: info@toiletcubiclesireland.ie Web: www.toiletcubiclesireland.ie

Product reference: formV toilet cubicles

Doors: 18mm/25mm chipboard faced both sides with high quality veneer

Core material: High density chipboard

Finish: Two coat A/C lacquer

Colour: Toilet cubicle Ireland veneer selection

Edge treatment: 10mm hardwood edge bonded to core board and over faced with veneer

Panels: 18mm/25mm chipboard faced both sides with high quality veneer

Core material: High density chipboard

Finish: Two coat A/C lacquer

Colour:Toilet Cubicles Ireland veneer selection

Edge treatment: 10mm hardwood edge bonded to core board and over faced with veneer

Pilasters: Two formed stainless steel angle profiles fixed to either side of the partition and set back from leading edge. Vertical edges full radius for safety.

Head Rail: 25mm diameter stainless steel tube fixed between partitions

Finish: Satin polished

Legs: Slim-line, adjustable cylindrical design, with concealed fixings positioned in line with the pilaster angles fixed directly into the partition core.

Ironmongery & Accessories: Adjustable pivot hinges/Buffered coat hook/DDA compliant lever operated indicator bolt with circular face plate and emergency release facility/Concealed continuous ‘T’ section partition fixings.

Finish/ Colour: Stainless steel or stainless steel effect.

Dimensions: Unless stipulated here dimensions are as the technical data provided for formV

Other requirements: Complete with outward opening doors to ambulant and enlarged cubicles as requested. Cubicles with inward opening doors can be set out to maintain 450mm diameter manoeuvring space within the cubicle, this may require an extended pilaster detail