K32 PANEL CUBICLES

To be read with preliminaries and general conditions

Manufacturer: Toilet Cubicles Ireland, Unit 15 Dinore Business pk, Donore Rd, Drogheda, Co Louth. Ph /fax 041-9818148

Email: info@toiletcubiclesireland.ie Web: www.toiletcubiclesireland.ie

Product reference: liquid toilet cubicles

Doors: 12/13mm solid grade laminate (SGL) same colour both sides

Core material: Not required self supported board black core (SGL)

Finish: Subject to SGL manufacturer selected

Colour: Toilet cubicles Ireland SGL selection or specified colours subject to size

Edge treatment: Machined smooth profile or square (Black core always visible)

Panels: 12/13mm solid grade laminate (SGL) same colour both sides

Pilasters: 12/13mm solid grade laminate (SGL) same colour both sides

Core material: Not required self supported board black core (SGL)

Finish: Subject to SGL manufacturer selected

Colour: Toilet Cubicles ireland SGL selection or specified colours subject to size

Edge treatment: Machined smooth profile or square (Black core always visible)

Head Rail: Rigid polished aluminium section with bull-nosed leading edge

Finish: Polished

Legs: Tubular polished aluminium design, through fixed into front of pilaster. Adjustable to accommodate varying floor levels

Ironmongery & Accessories: Aluminium pivot hinges/Coat hook/DDA compliant slide operated indicator bolt with elliptical face plate/Emergency release facility. Channel bracket partition fixings.

Finish/Colour: Polished Aluminium

Dimensions: Unless stipulated here dimensions are as the technical data provided for liquid

Other requirements: Complete with outward opening doors to ambulant and enlarged cubicles as requested. Cubicles with inward opening doors can be set out to maintain 450mm diameter manoeuvring space within the cubicle, this may require an extended pilaster detail