K13 PANEL LINING SYSTEMS (IPS) Compact/solid Grade Laminate

To be read with preliminaries and general conditions

Manufacturer:Toilet Cubicles Ireland, Unit 15 Donore Business pk,Donore Rd,Drogheda,

Co Louth Ph/ Fax 01-41-9818148

Email:info@toiletcubiclesireland.ie www.toiletcubiclesireland.ie

Product reference: Compact grade laminate full height duct/access panels

Panels: 12mm/13mm solid grade laminate made to measure panels, full height panel sets

Core material: Not required self supported board black core

Facing/Finish: Subject to SGL manufacturer selected

Colour: Toilet Cubicles Ireland SGL selection

Edge treatment: Machined smooth profile or square (Black core always visible)

Substrate: Treated softwood framework notched, screwed made to measure and site assembled.

Fixing of panels: Concealed Keku lift off or push fit clips/brackets

Joint treatment: Supplied with horizontal and or vertical flash gap strips in HPL laminate

Moisture content at time of fixing: As recommended by fabricator to suit environmental conditions as clause. Consult with Toilet Cubicles ireland for details.

Accessories: Fixing clips, flash gap laminate strips or (19mm bonded board option surcharge)

Dimensions: Unless stipulated dimensions of panels as the technical data provided for SGl duct  panels

Other requirements: Cut outs and holes through panels marked on site by builder. Sanitary ware schedule for panel splits and to assist in access panels being easily removed in line with CDM guidelines