K13 PANEL LINING SYSTEMS (IPS) HGL Laminate

To be read with preliminaries and general conditions

Manufacturer: Toilet Cubicles Ireland, Unit 15 Donore Business Pk, Donore Rd, Drogheda, Co Louth. Ph/fax 041-9818148.

Email: info@toiletcubiclesireland.ie  Web: www.toiletcubiclesireland.ie

Product reference: HGL full height duct/access panels

Panels: 20mm HPL faced made to measure panels, full height panel sets

Core material: Moisture resistant 650kg/m3 chipboard to V313

Facing/Finish: Subject to HPL manufacturer selected

Colour: Toilet Cubicles Ireland HPL selection card

Edge treatment: Two edges post formed two edges lipped with matching/contrasting 1mm PVC

Substrate: Treated softwood framework notched, screwed made to measure and site assembled.

Fixing of panels: Concealed Keku lift off or push fit clips/brackets

Joint treatment: Supplied with horizontal and or vertical flash gap strips in HPL laminate

Moisture content at time of fixing: As recommended by fabricator to suit environmental conditions as clause. Consult with Toilet Cubicles Ireland for details.

Accessories: Fixing clips, flash gap laminate strips or (19mm bonded board option surcharge)

Dimensions: Unless stipulated dimensions of panels as the technical data provided for Toilet Cubicle Ireland duct Panels

Other requirements: Cut outs and holes through panels marked on site by builder. Sanitary ware provided by others.