## Standard Locker Range ( Mild Steel).

Our standard locker range is available in various configurations and sizes ranging from full length units to multi-compartment units offering storage and security for up to six people (1-6 door lockers).

With various locker width options available as standard, this mild steel locker provides enough permutations to satisfy the most demanding of requirements.

With a comprehensive range of modern colours and the option of stands, stands with seating, sloping tops and ventilation, such outstanding versatility finds an immediate cost effective application in a whole variety of environments. Also available with Solid Grade Laminate doors for improved looks and security.

SPECIFICATION SHEET:

FULL LENGTH LOCKERS

Strength and Security with Style

Sturdy Construction: Door frame constructed from heavy gauge mild steel of press formed channel section.

Door Strength: Full length door stiffeners for extra door rigidity and three ‘five knuckle’ semi-concealed

hinges.

Style: Attractive and functional locker design.

Colour: Automated paint plant ensures consistent high quality finish in a wide range of modern

colours.

Detailed Product Specification

Nesting: Lockers can be supplied as single units or nested in groups during the manufacturing process.

All lockers are holed in back and sides to enable them to be bolted together into rows or back

to back to suit your requirements. Note: When preparing locker room layouts allow

approximately 4 mm extra for each nest for rivet heads at the sides of lockers in each row.

Construction: Spot welded and pop riveted.

Material: Mild steel Powder Coated.

Door Frame Assembly: Comprising two uprights manufactured from heavy gauge mild steel of press formed channel section; top and bottom cross members which are designed to create door stops. Spot

welded construction produces a rigid frame enabling door clearances to be maintained in

accordance with British Standard requirements. The top cross member is provided with a

series of ventilation slots.

Doors: Doors are attached to the right hand side of door frame upright with three ‘five knuckle’ semiconcealed

hinges. Doors are fitted with a plastic escutcheon plate around the lock, which can

also act as a name card/locker number holder. The inside of the door has a full length vertical

‘stiffener’ to provide greater rigidity. Two rubber buffers are fitted to the top and bottom

corners of the door for quiet closure.

Bottom: The bottom is formed as a 60 mm high plinth. All edges have return bends and the front and

rear edges drilled for fitting to stands or stands with seat.

Shelf: The lockers are fitted with a shelf 315 mm from the top, giving a clear 250 mm opening,

allowing adequate space for the average crash helmet with chin protector, or other articles.

Hook & Hanger Rails: A coat hook is located each side of the main compartment under the shelf; for lockers over 300 mm deep a plastic coated clothes hanger rail is also fitted.

Locking: Standard options are either 10 disc tumbler cam lock in mastered suite with two keys to each

lock or, at no extra cost, a latch lock for the user’s own padlock (recommended padlock shank

dimensions 6 mm).

As an optional extra for added security we can supply full reach espagnolette bolts giving

three point locking (ie, top, bottom and centre) with either of the standard locking options.

We can also supply, as an optional extras, a wide range of locking options, please ask for

details.

Nest of 1

Nest of 2

Nest of 3

Ventilation: Ventilation is provided by a series of unique ventilation slots in the top cross member.

Paint Finish: Five stage automatic degreasing and phosphating process to remove surface contamination.

This base gives improved adhesion and humidity resistance. The powder is electrostatically

applied prior to oven baking at the appropriate temperature.

Colour Range: Standard locker frame Powder Coated colours is: “Ice”. Standard door colours are: “Ice”,

“Black”, “Rockpool”, “Smoke”, “White”, “Skye”, “Yellow”, “Royale”, “Forest” and “Cherry”. Exact colour samples are available.

OPTIONAL EXTRAS: The following can be supplied at an additional cost and, if included, will be specified in the quotation.

Three Point Locking: The system provides effective and secure latching, allowing locking at three positions.

Perforation: Most parts of the locker can be perforated with the unique  perforation profile.

Where Full Length Lockers have perforated doors it is strongly recommended that three point

locking be fitted for added security.

Locker Numbering: a) Number Label – Made of silver polyester, with a permanent, self-adhesive back. Numbers are printed in black and can comprise one to four digits including letters.

b) Number Plate – Made of laminated plastic, white numbers on black, numbers can comprise

one to four digits.

c) Number Discs – Laminated plastic 25 mm diameter, white numbers on black, numbers can

comprise one to four digits. The disc is holed and a split key ring is provided.

Stands/with Seats: Lockers can be provided with either stands or stands with seats with or without adjustable

feet. Please refer to Specification Sheet S015.

Sloping Tops: Lockers can be manufactured with a sloping top. Gradient 1:3, ie

300 mm deep unit increased height at rear 100 mm

380 mm deep unit increased height at rear 126 mm

450 mm deep unit increased height at rear 150 mm

End Panels: For aesthetic appearance and to protect row ends, specifically designed end panels are

available.

Installation: Toilet Cubicles Ireland offer a full installation service for its products.

Bespoke: We have the ability to customise our products to meet your requirement and space, providing solutions for awkward corners, uneven floors or even curved walls.

Health & Safety: Lockers must be firmly secured to wall or floor and fixed together in runs for safety purposes. If applicable, install in accordance with specific product instructions.

􀂃 All dimensions are nominal.

􀂃 To enable us to interpret your requirements accurately, please state at time of enquiry/order the choice of locker type, colour, locking and nesting arrangement and delivery requirement.

􀂃 The products described in this specification sheet herein are the subjects of patent, trademark, design and copyright protection or application thereof.

􀂃 In the interest of efficiency and service to our customers, the company reserves the right to modify the specifications of any of its products.