Shadow tech Shower glass cubicle

Clean curved appearance of  powder coated aluminium elliptical front profiles and headrail.

• Panels and doors in compact grade laminate, solid surfacing, toughened glass.

• The cubicles are suitable for wet or dry use.

• The extruded aluminium 100mm x 28mm elliptical headrail, mechanically joined to elliptical aluminium pilaster profiles with

screwport connections to form a structural framework including end caps.

• Door frame with  anti-finger trap detail.

• Partition panels supported on adjustable legs mechanically connected to pilaster components.

• Full length channels are used to attach partition and pilaster panels to walls.

• Partition panels secured into pilaster hex screws

Panels & Doors to Wet or Dry Areas:

• 12/13mm compact grade laminate.

• 12mm solid surfacing material.

• 10mm toughened float or textured cast glass, ceramic paint finish, for W.C. and changing cubicles or translucent for shower cubicles.

• Toughened and laminated float glass with ceramic paint to one internal face. This produces equal colour shade to both outer surfaces.

Hardware & Fittings:

• Adjustable aluminium floor attachments.

• Solid coloured nylon door furniture.

• Standard handle assembly.

• Optional satin anodised aluminium door latch set with sliding action.

• Full length pivot hinge fall open/close.

• With satin anodised aluminium or stainless steel ironmongery options.

• 1 coat hook per cubicle fixed to door frame.

• 2 coat hooks to DDA compliant cubicles.

• DDA compliant handle set with lever action turn and horizontal grab handles.

• Door closer available for outward opening cubicle doors.

High Level Specification:

• Suitable for wet areas with high volume use, public toilets, changing cubicles (wall mounted).

• Panels and doors in 12/13mm compact grade laminate.

• Hardware in stainless steel or satin anodised aluminium or power coated.